Class Assignment #1 – Structual Design 1. semester

No. 1

There is given a beam which is loaded with a mass of 2700 kg as shown on figure 1.

- Draw the static construction (remember to add 10 cm in each side to support depth).

- Calculate the reaction VA and VB

Imagine that the beam is supported with columns that can take a calculated pressure of

σcd = 1,50 N/mm2

- Under assumption that the columns are massive squared it is your task to calculate the width.

No. 2

Another beam is loaded with two masses. Mass one is 2700 kg and the other is 700 kg as shown on figure 2.

- Draw the static construction.

- Calculate the reaction VA and VB

Imagine that the beam is supported with columns that can take a calculated pressure of

σcd = 1,50 N/mm2

- Under assumption that the columns are massive squared it is your task to calculate the width.

No. 3

- Draw the static construction.

- Is the construction in balance? Documentation is required.

- Calculate the reaction VA and VB

Imagine that the beam is supported with columns that can take a calculated pressure of

σcd = 1,50 N/mm2

- Under assumption that the columns are massive as shown it is your task to calculate the width.

# Text boxes

2,50 m

B

2700 kg

5,50 m

A

b

b

2700 kg

2,50 m

4,50 m

B

A

1,00 m

700 kg

b

b

2000 kg

1400 kg

3,50 m

2,50 m

2,50 m

b

A

B

2xb