Class Assignment #2 – Structual Design 1. semester

No. 1

There is given a beam which is loaded with a force of 150 kN as shown on figure 1.

- Draw the static construction (remember to add 10 cm in each side to support depth).

- Calculate the reaction VA and VB

Imagine that the beam is supported with columns that can take a calculated pressure of

σcd = 2,20 N/mm2

- Under assumption that the columns are massive rectangular it is your task to calculate the width.

No. 2

Another beam is loaded with uniform load of 100 kN/m as shown on figure 2. (remember to add 10 cm in each side to support depth).

- Draw the static construction.

- Calculate the reaction VA and VB

Imagine that the beam is supported with columns that can take a calculated pressure of

σcd = 3,0 N/mm2

- Under assumption that the columns are circular it is your task to calculate the diameter.

No. 3

There is given a beam which is loaded with a diagonal force of 200 kN as shown on figure 3. (remember to add 10 cm to support depth in point A).

The angle to the horizontal is 60º

- Draw the static construction.

- Calculate the reaction VA and VB

Imagine that the beam is supported with a column in support B that can take a calculated pressure of σcd = 1,50 N/mm2

- Under assumption that the columns are massive as shown it is your task to calculate the width.

- In support A the beam is fastened with a rectangular massive iron anchor to the foundation. The thickness of the anchor is 5 mm, and the maximum calculated tension for the steel is

σcd = 184 N/mm2. How wide should the anchor be?

# Text boxes

B

F = 150 kN

4,00 m

A

b

4b

sd = 100 kN/m

3,50 m

B

A

Ø

width

5 mm

3,50 m

F = 200 kN

5,00 m

b

A

B

3b